## Slide 1
OAI O-RAN 7.2 Split
A Demo of End-to-End Emulation
and IQ Compression Evaluation
Single-host DU + O-RU + UE over real DPDK fronthaul — a platform to observe system trade-offs:
UL throughput · fronthaul load · latency · PRB / bandwidth · SNR · mobility
Jesse · 2026

## Slide 2
System Overview in the Demo
One host runs the whole 5G chain — real DPDK fronthaul, emulated radio
DU
nr-softmodem (PHY/MAC)
24 PRB · µ1 30 kHz · n77 4.05 GHz
O-RU
nr-oru (RU PHY)
O-RAN 7.2 split · IQ compression
UE
nr-uesoftmodem
1 UE · oaitun_ue1 · 10.0.0.x
O-RAN 7.2 FH
eCPRI · DPDK SR-IOV
VF0/1↑ VF2/3↓ · VLAN 3/4
vrtsim air
shared memory · IQ
TDL fading · AGC SNR
↕ NGAP / GTP-U
OAI 5GC (docker)
AMF · SMF · UPF · NRF
↕ iperf3 client (UE) -c 10.0.0.1
UL received here
(iperf3 server @ 5GC/UPF)
real-time channel
emulation (CPU)
NIC: Intel X710 (i40e) · 5 SR-IOV VFs · VF↔VF loopback (embedded VEB switch, no cable) | Fronthaul = real eCPRI packets over DPDK | Air = vrtsim shared-memory IQ
What we can sweep / evaluate
Parameter
What it controls in the demo
IQ width (8 / 9 / 12 / 16)
Fronthaul byte load (IQ compression)
RX target SNR (dB)
Radio link quality (time-domain AGC)
Antennas (1×1 → 4×4)
MIMO layers & fronthaul load multiplier
FH delivery window (µs)
Fronthaul timing / latency budget
Mobility (channel time-var.)
Time-varying fading
Bandwidth (PRB)
Cell bandwidth, 10 – 100 MHz
UL throughput = traffic RECEIVED at the 5GC (UPF), where the iperf3 server runs — the real goodput, not the UE's send rate (which over-reports, since the UE drops excess at the TUN).

## Slide 3
Baseline: 10 MHz Radio Bandwidth
The reference operating point — each later slide varies ONE knob and watches the trend
Measured — 1×1, 24 PRB µ1, ideal channel (UL received at 5GC/UPF, iperf3 UDP)
Config
IQ
FH total Mbps
UL Mbps
Jitter ms
UL loss
1×1 ideal
9
150.8
4.995
1.83
0.00%
1×1 ideal
9
150.8
5.004
—
—
1×1 ideal
16
254.0
5.006
—
—
UL throughput
~5.0 Mbps
UL loss
0.00 %
Jitter
~1.8 ms
UL symbols
100 %
FH load
150 / 254
Mbps (iq9/16)
This is the reference point. From here, each evaluation changes one parameter — IQ compression, SNR, MIMO, fronthaul latency, mobility, bandwidth — and we read the TREND in UL throughput, fronthaul load, latency and resource use.
The point of the demo is not 'it works' — it is that one host lets us sweep these knobs and SEE the trade-offs.

## Slide 4
Evaluation 1 — IQ Compression vs Fronthaul Load
Sweep IQ width 8→16 in one bringup · what does compression buy us?
Measured (single sweep, 1×1 ideal channel)
IQ width
FH total Mbps
UL Mbps
UL loss
8 (most compressed)
135.2
4.999
0.00%
9 (BFP default)
150.8
4.999
0.00%
12
197.4
5.001
0.00%
16 (uncompressed)
254.0
5.001
0.00%
Fronthaul load (bars) vs UL throughput (line)
FH Mbps
135
iq8
151
iq9
197
iq12
254
iq16
UL ~5.0 Mbps — flat
FINDING
Compressing IQ from 16→8 bits cuts fronthaul load 47%
(254 → 135 Mbps) with NO loss of UL throughput or quality.
Why UL stays flat:
the fronthaul link here has huge spare capacity (uses <5%), so saving FH bytes does not change the air throughput.
To expose a compression-vs-quality trade-off, constrain the FH pipe (Eval 4) or raise the load with MIMO / wider BW (Eval 3 & 6).

## Slide 5
Evaluation 2 — Link Quality (SNR) vs UL Throughput
Axis is TIME-DOMAIN RX SNR (the real channel SNR) injected by the vrtsim AGC
Time-domain SNR — AGC-controlled (validated)
TD SNR
UL Mbps
Jitter ms
20 dB
4.995
1.83
8 dB
2.148
4.92
Channel-model runs (ULSCH → time-domain)
ULSCH dB
TD dB
UL Mbps
32.8
~16
2.67
33.0
~16
2.83
35.9
~19
3.57
39.2
~22
4.96
42.3
~25
4.98
46.3
~29
4.98
10
15
20
25
30
1
2
3
4
5
Time-domain RX SNR (dB)
UL
Mbps
■ AGC-controlled (exact) ■ channel-model runs (converted)
Note: time-domain SNR = real channel SNR. The post-FFT (ULSCH) SNR reads ~17 dB higher from OFDM processing gain — so the channel-model runs (32–46 dB ULSCH) are shown at their true ~16–29 dB time-domain values.
FINDING: UL throughput tracks the real (time-domain) SNR monotonically — 20 dB → 5.0 Mbps, 8 dB → 2.1 Mbps — and jitter rises as SNR falls. The demo can sweep link quality on demand.

## Slide 6
Evaluation 3 — MIMO Scaling & Fronthaul Dimensioning
Add antennas (1×1 → 4×4) · how does fronthaul load grow?
Measured (iq9, 10 MHz, mobility channel)
Antennas
FH total Mbps
UL Mbps
Result
1×1
150.8
4.999
stable
2×2
301.5
4.98
stable
4×4
1016.1
4.998
works (compute-heavy)
Fronthaul total load (Mbps) scales with antenna count
FH Mbps
151
1×1
302
2×2
1016
4×4
FINDING
Fronthaul load scales ~linearly with antennas:
1×1 → 2×2 → 4×4 = 151 → 302 → 1016 Mbps.
Useful for dimensioning the FH link for a target MIMO order.
UL goodput stays ~5 Mbps across all configs — at this bandwidth the air scheduler, not the fronthaul, sets the rate.
4×4 real-time channel emulation is compute-heavy on a single host — it works but is near the box's CPU limit.

## Slide 7
Evaluation 4 — Fronthaul Timing Budget Sensitivity
Tighten the fronthaul delivery window · when does the link start to break?
Measured (2×2, iq9) — tightening the FH delivery deadline
FH window (µs)
Packets dropped
UL Mbps
Status
200 – 300
0
~5.0
clean
350
~8
4.7
first drops
400
~120
4.0
knee
450
~130,000
2.5
degraded
≥ 600
very high
0
FAIL
Packets dropped (log, bars) + UL Mbps (line)
0
250µs
~8
350µs
~120
400µs
~130k
450µs
crash
600µs
FINDING
There is a sharp 'knee' in the fronthaul timing budget:
the link is clean down to ~350 µs, then collapses between 400–450 µs (dropped packets jump ×1000, UL halves), and fails below the budget.
This is exactly the kind of timing-margin test you want before deploying on a real fronthaul link with finite latency.

## Slide 8
Evaluation 5 — Mobility / Time-Varying Channel
Sweep a time-varying fading channel at 3 / 60 / 120 km/h-equivalent
Measured (2×2, iq9, fading channel) · SNR = time-domain (real channel) SNR
Mobility
TD SNR dB
UL Mbps
Result
3 km/h
~16
2.67
ok (low-SNR run)
3 km/h
~22–29
~4.98
ok
60 km/h
~21–27
4.4 – 4.98
ok
120 km/h
—
0
FAIL — DL sync cannot lock
FINDING: at good SNR the link is robust to mobility — UL stays ~5 Mbps up to 60 km/h-equivalent. At 120 km/h the very fast fading prevents the UE from locking onto the downlink.
Scope note: the demo models mobility as a channel time-variation factor, not a true Doppler shift, so this evaluates link robustness to fast fading rather than precise velocity effects.
Also: uplink channel estimation is per-slot, so uplink data is largely insensitive to channel aging — the mobility effect shows up mainly in initial downlink synchronisation.

## Slide 9
Evaluation 6 — Bandwidth Scaling & Fronthaul Headroom
How much fronthaul headroom is there, and what limits wider bandwidth?
Fronthaul capacity vs actual demo load
Fronthaul
Capacity / load
Utilisation
Link capacity (measured)
6.36 Gbps
—
10 MHz · 1×1 · iq9
0.15 Gbps
2 %
10 MHz · 4×4 · iq16
1.02 Gbps
16 %
Wider bandwidth — current status
Bandwidth
Status
10 MHz (24 PRB)
works ✓
40 MHz (106 PRB)
not yet — needs PHY rework
≥ 50 MHz / 100 MHz
not yet — compute / PHY limits
FINDING
The fronthaul is massively over-provisioned — the demo uses at most 16% of link capacity, so fronthaul bandwidth is never the bottleneck.
The cell currently runs at 10 MHz. Going wider is a known next step that needs PHY-layer rework and more real-time compute — not more fronthaul.

## Slide 10
What This Demo Can Evaluate
One platform, six evaluation axes
Evaluation
What we sweep
What we find
IQ compression
IQ width 8→16
FH load −47% at iq8, no UL loss
Link quality
RX SNR (AGC)
UL tracks SNR: 5.0 → 2.1 Mbps (20→8 dB)
MIMO scaling
1×1 → 4×4 antennas
FH load scales ×N (151 → 1016 Mbps)
FH timing budget
FH delivery window
sharp knee at 400–450 µs
Mobility
fading speed 3–120 km/h
robust ≤60 km/h; DL sync fails at 120
Bandwidth / FH
PRB / antennas / iq
FH ≤16% utilised — large headroom
Take-away: one host lets us SEE the system trade-offs — compression vs fronthaul load, SNR vs throughput, MIMO vs fronthaul load, timing budget vs link, bandwidth vs fronthaul headroom — with real DPDK fronthaul and real over-the-air goodput.

## Slide 11
Key Findings
All numbers measured on the demo (UL received at the 5GC, iperf3 UDP)
Metric
Result
Baseline UL (10 MHz, 1×1, iq9)
5.0 Mbps · 0% loss · 1.8 ms jitter
IQ compression iq16 → iq8
FH load 254 → 135 Mbps (−47%), UL unchanged
UL vs SNR
20 dB → 5.0 Mbps / 8 dB → 2.1 Mbps
MIMO FH load 1×1 / 2×2 / 4×4
151 / 302 / 1016 Mbps
FH timing knee
clean ≤350 µs → collapses 400–450 µs
Mobility robustness
stable ≤60 km/h-equiv; fails at 120
Fronthaul link capacity
6.36 Gbps — demo uses ≤16%
Bottom line: a single-host O-RAN 7.2 split that lets us explore system-level trade-offs across compression, SNR, MIMO, latency, PRB / bandwidth, and mobility.