## Slide 1
OAI O-RAN 7.2 Split
A Demo of End-to-End Emulation
and IQ Compression Evaluation
Single-host DU + O-RU + UE over real DPDK fronthaul — a platform to observe system trade-offs:
UL throughput · fronthaul load · latency · PRB / bandwidth · SNR · mobility
Jesse · 2026

## Slide 2
System Overview in the Demo
One host runs the whole 5G chain — real DPDK fronthaul, emulated radio
DU
nr-softmodem (PHY/MAC)
24 PRB · µ1 30 kHz · n77 4.05 GHz
O-RU
nr-oru (RU PHY)
O-RAN 7.2 split · IQ compression
UE
nr-uesoftmodem
1 UE · oaitun_ue1 · 10.0.0.x
O-RAN 7.2 FH
eCPRI · DPDK SR-IOV
VF0/1↑ VF2/3↓ · VLAN 3/4
vrtsim air
shared memory · IQ
TDL fading · AGC SNR
↕ NGAP / GTP-U
OAI 5GC (docker)
AMF · SMF · UPF · NRF
↕ iperf3 client (UE) -c 10.0.0.1
UL received here
(iperf3 server @ 5GC/UPF)
real-time channel
emulation (CPU)
NIC: Intel X710 (i40e) · 5 SR-IOV VFs · VF↔VF loopback (embedded VEB switch, no cable) | Fronthaul = real eCPRI packets over DPDK | Air = vrtsim shared-memory IQ
What we can sweep / evaluate
Parameter
What it controls in the demo
IQ width (8 / 9 / 12 / 16)
Fronthaul byte load (IQ compression)
RX target SNR (dB)
Radio link quality (time-domain AGC)
Antennas (1×1 → 4×4)
MIMO layers & fronthaul load multiplier
FH delivery window (µs)
Fronthaul timing / latency budget
Mobility (channel time-var.)
Time-varying fading
Bandwidth (PRB)
Cell bandwidth, 10 – 100 MHz
UL throughput = traffic RECEIVED at the 5GC (UPF), where the iperf3 server runs — the real goodput, not the UE's send rate (which over-reports, since the UE drops excess at the TUN).

## Slide 3
Evaluation 1 — IQ Compression vs Fronthaul Load
Sweep IQ width 8→16 in one bringup · what does compression buy us?
Measured (single sweep, 1×1 ideal channel)
IQ width
FH total Mbps
UL Mbps
UL loss
8 (most compressed)
135.2
6.999
0.00%
9 (BFP default)
150.8
6.999
0.00%
12
197.4
7.001
0.00%
16 (uncompressed)
254.0
7.001
0.00%
Fronthaul load (bars) vs UL throughput (line)
FH Mbps
135
iq8
151
iq9
197
iq12
254
iq16
FINDING
Compressing IQ from 16→8 bits cuts fronthaul load 47%
(254 → 135 Mbps) with NO loss of UL throughput or quality.
Why UL stays flat:
the fronthaul link here has huge spare capacity (uses <5%), so saving FH bytes does not change the air throughput.
To expose a compression-vs-quality trade-off, constrain the FH pipe (Eval 4) or raise the load with MIMO (Eval 3).
Test conditions: 24 PRB · n77 4049.76 MHz (≈4.05 GHz) · numerology µ1 (30 kHz SCS) · MCS 28 (64QAM) · post-proc SNR ≈ 38.8 dB (iq9)
TDD & scheduler: D·M·D·D·U = 1 of 5 UL slots(20%), theoretical UL ≈ 7 Mbps

## Slide 4
Evaluation 2 — Link Quality (SNR) vs UL Throughput
Axis is TIME-DOMAIN RX SNR (the real channel SNR) injected by the vrtsim AGC
Time-domain SNR — AGC-controlled (validated)
TD SNR
UL Mbps
Jitter ms
20 dB
6.99
1.83
8 dB
3.01
4.92
Channel-model runs (ULSCH → time-domain)
ULSCH dB
TD dB
UL Mbps
32.8
~16
3.74
33.0
~16
3.96
35.9
~19
5.00
39.2
~22
6.94
42.3
~25
6.97
46.3
~29
6.97
10
15
20
25
30
3
4
5
6
7
Time-domain RX SNR (dB)
UL
Mbps
■ AGC-controlled (exact) ■ channel-model runs (converted)
Note: time-domain SNR = real channel SNR. The post-FFT (ULSCH) SNR reads ~17 dB higher from OFDM processing gain — so the channel-model runs (32–46 dB ULSCH) are shown at their true ~16–29 dB time-domain values.
FINDING: UL throughput tracks the real (time-domain) SNR monotonically — 20 dB → 7.0 Mbps, 8 dB → 2.9 Mbps — and jitter rises as SNR falls. The demo can sweep link quality on demand.

## Slide 5
Evaluation 3 — MIMO Scaling & Fronthaul Dimensioning
Add antennas (1×1 → 4×4) · how does fronthaul load grow?
Measured (iq9, 10 MHz, mobility channel)
Antennas
FH total Mbps
UL Mbps
Post-processing SNR (dB)
1×1
150.8
6.999
38.8
2×2
301.5
6.97
42.5
4×4
1016.1
6.997
44.2
Fronthaul total load (Mbps) scales with antenna count
FH Mbps
151
1×1
302
2×2
1016
4×4
FINDING
Fronthaul load scales ~linearly with antennas:
1×1 → 2×2 → 4×4 = 151 → 302 → 1016 Mbps.
Useful for dimensioning the FH link for a target MIMO order.
UL goodput stays ~7 Mbps across all configs — at this bandwidth the air scheduler, not the fronthaul, sets the rate.
4×4 real-time channel emulation is compute-heavy on a single host — it works but is near the box's CPU limit.
38.8
42.5
44.2
● Post-processing SNR (dB) — rises with RX combining gain
Theoretical RX-combining gain ≈ +3 dB per antenna doubling
→ +0 / +3 / +6 dB (1×1 / 2×2 / 4×4) · measured +0 / +3.7 / +5.4 dB ✓

## Slide 6
Evaluation 4 — Fronthaul Timing Budget Sensitivity
Tighten the O-RU downlink U-plane reception window — O-RAN T2a · when does the link break?
Measured (2×2, iq9) — tightening the FH delivery deadline
FH window · T2a_min (µs)
Packets dropped
UL Mbps
Status
200 – 300
0
~7.0
clean · BASELINE
350
~8
6.6
first drops
400
~120
5.6
knee
450
~130,000
3.5
degraded
≥ 600
very high
0
FAIL
Packets dropped (log, bars) + UL Mbps (line)
0
250µs
~8
350µs
~120
400µs
~130k
450µs
crash
600µs
FINDING
There is a sharp 'knee' in the fronthaul timing budget:
the link is clean down to ~350 µs, then collapses between 400–450 µs (dropped packets jump ×1000, UL halves), and fails below the budget.
This is exactly the kind of timing-margin test you want before deploying on a real fronthaul link with finite latency.
7.0
6.6
5.6
3.5
0
● UL throughput (Mbps) — baseline ~7.0, collapses as the FH window tightens
WHY THROUGHPUT DROPS
A UL packet that misses the FH deadline is dropped → NACK → HARQ retransmit. The gNB's outer-loop link adaptation also reads these FH-late drops as radio errors and backs off MCS — so throughput collapses far faster than the raw drop-rate (≈5% late → UL roughly halves).
FH window = O-RAN T2a (T2a_min_up): latest a DL U-plane IQ packet may reach the O-RU before its on-air time (Fig 4.4.1-1, R2→Ra). Tightening it ≡ adding real fronthaul transport delay — on-air lead here ≈ 430 µs, so the knee lands at 400–450 µs.

## Slide 7
Evaluation 5 — Mobility / Time-Varying Channel
Sweep a time-varying fading channel at 3 / 60 / 120 km/h-equivalent
Measured (2×2, iq9, fading channel) · SNR = time-domain (real channel) SNR
Mobility
RX SNR dB
UL Mbps
Result
3 km/h
~16
3.74
ok
3 km/h
~22–29
~6.97
ok
60 km/h
~21–27
6.2 – 7.0
ok
120 km/h
—
0
FAIL — DL sync cannot lock
FINDING: at good SNR the link is robust to mobility — UL stays ~7 Mbps up to 60 km/h-equivalent. At 120 km/h the very fast fading prevents the UE from locking onto the downlink.
Scope note: the demo models mobility as a channel time-variation factor, not a true Doppler shift, so this evaluates link robustness to fast fading rather than precise velocity effects.
Also: uplink channel estimation is per-slot, so uplink data is largely insensitive to channel aging — the mobility effect shows up mainly in initial downlink synchronisation.

## Slide 8
What This Demo Evaluates — Key Findings
One host = a full end-to-end 5G system (UE · O-RU · real O-RAN 7.2 fronthaul · O-DU · 5G core) — every number below measured on a live link
Metric
Result
Baseline UL (10 MHz, 1×1, iq9)
7.0 Mbps · 0% loss · 1.8 ms jitter
IQ compression iq16 → iq8
FH load 254 → 135 Mbps (−47%), UL unchanged
UL vs SNR
20 dB → 7.0 Mbps / 8 dB → 2.9 Mbps
MIMO FH load 1×1 / 2×2 / 4×4
151 / 302 / 1016 Mbps
FH timing knee
clean ≤350 µs → collapses 400–450 µs
Mobility robustness
stable ≤60 km/h-equiv; fails at 120
Fronthaul link capacity
6.36 Gbps — demo uses ≤16%
Bottom line: this tool runs a FULL end-to-end 5G system on a single host — including a real O-RAN 7.2 DPDK fronthaul — so compression, link quality, MIMO, FH timing, mobility and FH headroom are all evaluated together, on a live link rather than modelled.